## Slide 1: IAQ Problem Prevention
NH Health Officer’s Association
Spring Conference
May 25, 2011
Phil Alexakos, MPH, REHS
Chief of Environmental Health and Emergency Preparedness
Manchester Health Department

## Slide 2: Mold Prevention
Moisture, Moisture, Moisture!!!!!

## Slide 3: Routine Maintenance
Filter Changes
  Frequency
  MERV rating vs. Air Flow
Ceiling Tiles
  Water staining
    Old or New??
    Missing and Why?

## Slide 4: Routine Maintenance
Plumbing Fixture Leaks
Condenser Drip Pans
Water infiltration
  Ground (sumps)
  Door sweeps
  Walls
  Below Grade Spaces!!

## Slide 5: Best Practices
Control Moisture
  Humidity
    Must be less than 60 %
    Ideally between 30-50%
  Exterior Grading
    Water should be directed away from the building
  Temperature Contrast
    Poor insulation, venting

## Slide 6: Best Practices
Control Temperature
ASHRAE STANDARD 55-1981 Thermal Environmental Conditions for Human Occupancy
Relative Humidity | Winter temperatures O F | Summer temperatures O F
30% | 68.5-76.0 | 74.0-80.0
40% | 68.5-75.5 | 73.5-79.5
50% | 68.5-74.5 | 73.0-79.0

## Slide 7: Best Practices
Control Spores
  Door Mats
  HEPA Filtration Vacuuming
  Carpet Assessment
    Wet?
    Fraying

## Slide 8: Best Practices
Assess HVAC system at least quarterly
  Returns and Exhaust are unobstructed
  Check duct work and insulation for moisture
  Assure that moisture producing equipment is vented
    Dishwashers etc.

## Slide 9: Best Practices
Staff should be encouraged to report any signs of water damage
  Time is of the Essence
  After 48 Hours the Hazards Increase

## Slide 10: Visible Mold
Remove the Source of Moisture!!
  If you just treat the surface or paint over it…
  I’ll BE BACK!!

## Slide 11: Questions & Answers